## Slide 1: Homework Exercise 02
Geodetic Earth Observation, WS 2022/23
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 2: Structure of the presentation
Introduction
Data processing
  Selection of a region of interest
  Pre-processing the monthly solutions
  Calculation of unfiltered equivalent water heights (EWH)
  Filtering of the spherical harmonic coefficients
  Computation of a time series of region averages
  Interpolation of missing GRACE months
  Estimation of linear mass trend
Results and discussion
Conclusion and perspective
Bibliography
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 3: 1. Introduction
The continental mass balance changes constantly
  Seasonal changes
  Changes due to global warming
  Changes due to other human activity
These mass changes can be observed using 3 methods
  input-output method
  volumetric method
  gravimetric method
Christopher Mahn, Silas Teske, Joshua Wolf
Sasgen et al. (2020)

## Slide 4: 1. Introduction
Mass changes can be observed using gravimetric methods
  t0 = more mass = higher gravitational force
  t1 = less mass = lower gravitational force
Equivalent water heights (EWH)
Christopher Mahn, Silas Teske, Joshua Wolf
Eicker (2022)

## Slide 5: 1. Introduction
Necessary Steps while processing the data:
  Removal of the static gravity field
  Calculation of unfiltered equivalent water heights
    Using the load love numbers for approximating the glacial isostatic adjustment (GIA)
  Filtering of the spherical harmonic coefficients
    Gaussian filter with various filter radii choose one
  Computation of a time series of region averages
  Interpolation of missing GRACE months by inserting the average of the previous and the successive mean EWH
  Estimation of linear mass trend of the interpolated series
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 6: 2. Data processing
Python scripts and a library for different sub-tasks:
  main.py
  data_processing.py
  functions.py
  data_plotting.py
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 7: 2. Data processing
Python scripts and a library for different sub-tasks:
  main.py
  data_processing.py
  functions.py
  data_plotting.py
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 8: a) Selection of a region of interest
Canadian Province of British Columbia

## Slide 9: b) Pre-processing the monthly solutions
Removed the static gravity field ITSG-Grace2018s.gfc
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 10: c) Calculation of unfiltered EWH
P
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 11: d) Filtering of the spherical harmonic coefficients
P
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 12: e) Computation of a time series of region averages
P
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 13: f) Interpolation of missing GRACE months
P
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 14: g) Estimation of linear mass trend
P
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 15: 3. Results and discussion
Christopher Mahn, Silas Teske, Joshua Wolf
P

## Slide 16: 4. Conclusion and perspective
P
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 17: Bibliography
Sasgen, I., Wouters, B., Gardner, A.S. et al. (2020): Return to rapid ice loss in Greenland and record loss in 2019 detected by the GRACE-FO satellites. Communications Earth & Environment 1 (8). Springer Nature.
Christopher Mahn, Silas Teske, Joshua Wolf

## Slide 18: 1. Introduction ????
Mass changes can be observed using gravimetric methods
  t0 = more mass = higher gravitational force
  t1 = less mass = lower gravitational force
Problem: Glacial isostatic adjustment (GIA)
  Viscoelastic reaction of earth‘s crust to changing loading masses
GIA is difficult to model
  Ice cover of last glacial maximum is not exactly known
  Dependent on the structure and physical characteristics of the earth’s mantle and crust
Christopher Mahn, Silas Teske, Joshua Wolf
Eicker (2022)